## Slide 1
ELI Beamlines
Control System Overview
Author: Radek Horálek
2/3/2025
Date:

## Slide 2
Contents
  Introduction
  Scope of the architecture
  Communication protocols
  HW needs
  RIO utilization
  Integration
  GUIs
  Build & Deploy
  Archiving

## Slide 3
Introduction
  Templates and source code versioning ensure fast deployment of new solutions in the lab
      MySQL, P4V Helix
      ELI Controls and ELI.lib (developed in LabVIEW)
  EPICS commands and data are supported

## Slide 4
Scope of the Architecture (I)

## Slide 5
Scope orf the Architecture (II)
Each RMC contains several Input-Output Controllers (IOC)
Each IOC contains processes
Chart: Sales

## Slide 6
Communication Protocols - AMC
  AMC (Asynchronous Message Communication)
    UDP based
    Sending commands from Developer GUIs to IOCs
  Network Streams
    Handle reliable transfers on top of modified TCP/IP
    Used for developer GUIs
    Streams are wrapped into the architecture
  CA (Channel Access)
    Used by EPICS 3.14
    Enables transfer of data using TCP/IP with additional features

## Slide 7
HW Needs
  Supported OS: ETS PharLap, NI RT Linux, Win10
  RMC 8354 (matured)
  KISS 1U Short V3 CFL
      Intel i7-9700E (8Core/2,6GHz)
      8GB DIMM DDR4 2666
    NI cRIO (different types)
  Real-time controllers can be virtualized

## Slide 8
RIO Utilization
  NI 9149 is the most common type (Ethernet RIO)
  Programmatic interaction with FPGA front panel for slow data
  FIFOs for fast data
  Both DAQ and state machine control are applicable on FPGA

## Slide 9
Integration (I)
  Process data -> IOC -> EPICS
  EPICS GUIs allow access to multiple IOCs through EPICS layer

## Slide 10
Integration (II)
  Database contains information about all the PVs and IOCs
  PVs require server information
  IOCs require INI and CFG configurations that define their functionality
02.08.2021
10

## Slide 11
Integration (III)
  Database access is provided using DB Config Access.vi
  Configuration history can then be used to backtrack in time what changes might have had an effect on the system
02.08.2021
11

## Slide 12
Integration (IV)
  Data is published using a LabIOC server which is present on all machines
02.08.2021
12

## Slide 13
GUIs (I)
  A central launcher is used to access developer GUIs
02.08.2021
13

## Slide 14
GUIs (II)
  EPICS GUIs use a special template that defines their appearance but allows various PVs to be added as data sources
  This is stored in the database and it is modifiable using an editor
02.08.2021
14

## Slide 15
Build & Deploy
  Central app allows access to various tasks
02.08.2021
15

## Slide 16
Build & Deploy (Build)
02.08.2021
16

## Slide 17
Build & Deploy (Deploy)
02.08.2021
17

## Slide 18
Archiving
02.08.2021
18
  Raw archived data are stored centrally for all lasers

## Slide 19
Thank you for your attention!
Author: Radek Horalek
(radek.horalek@eli-beams.eu)